## Slide 1
What is "Latch Contention”?
And why should I care?
Tom Bascom, White Star Software
Monday 2:15pm
Abstract: Come to this session to learn what a latch is, how it enables reliable and highly concurrent access to your database and why you should be wary of "too many cores"!

## Slide 2: What is “Latch Contention”?
It isn’t just for Minty Fresh Breath!
Tom Bascom, White Star Software tom@wss.com
And why should I care?

## Slide 3: What is a “latch” anyway?
A lock on shared memory
Also known as a MUTEX (Mutual Exclusion) Lock
Or a “spin lock”
Latches must be implemented as an *atomic* operation and they protect activities that must behave as atomic actions
At the machine code level this is often a “Test and Set” or a “Compare and Swap” instruction

## Slide 4: Why are latches important?
Latches coordinate access to shared memory
The use of latches enables highly performant concurrent access
  Alternate methods of locking shared memory (such as semaphores) are *much* slower
Because latches are shared:
  They can be a source of contention and performance bottlenecks
  They can also be a source of database crashes

## Slide 5: When Might I See “Latch Contention”
Usually not until after you have eliminated IO as a bottleneck
The amount of memory in servers has grown enormously
  Terabyte memory in servers is becoming common
  Which means that it is possible to fit your whole DB into –B
  Even without doing that, the “working set” of a DB is usually much less than the full db size
It is becoming increasingly common to see latch contention bottlenecks

## Slide 6: I’m just doing FIND NO-LOCK
You still need to pay attention
When you access data, whether to read or write, you access shared memory
Latches keep shared memory consistent and have nothing to do with record locks
  (although latches are used to keep the lock table consistent)

## Slide 7: An Example: The LRU Chain
LRU = Least Recently Used
This is how the DB Engine decides which block to replace when it needs to read a new block from disk
Whenever any block is referenced we move it to the head of the LRU chain (a ”linked list”)
This results in unused blocks gradually moving to the tail of the chain and frequently used blocks staying towards the head

## Slide 8: Updating the LRU Chain
Most Recently Used
Least Recently Used

## Slide 9: Updating the LRU Chain
Most Recently Used
Least Recently Used

## Slide 10: LRU Chain
To move an entry you need to update multiple pointers in shared memory
If someone else updates the list at the same time, that will corrupt the list
So in order to safely update the list it must be locked!
Because many people need to do this, the lock forms a bottleneck

## Slide 11: So what does –spin have to do with it?
To obtain a latch you “test and set” until you succeed
This can consume a lot of CPU cycles
But it usually takes less time and fewer resources than waiting for a semaphore
The –spin value is the number of times to try before giving up
If you “spin out” then your process will nap
The length of your nap increases progressively from –nap to –napmax until you eventually succeed and get the latch!

## Slide 12: Latch requests & naps: ProTop
┌─────────────────── Latch Activity ────────────────────┌─────────────── Resource Waits ───────────────┌────────────────── TXE Locks & Waits ──────────────────┐
│ Latch Type Hlder QHold Requests Waits v Lock% │ Resource Requests Waits v Lock% │ TXE Type Locks Waits v Lock% ConLk% ConLk ConWt │
│ ──────────────────────────────────────────────────── │ ─────────────────────────────────────────── │ ──────────────────────────────────────────────────── │
│ >LRU ? 21 -1 2023998 609 99.97% │ >Shared Memory 5622036 7709615 -37.13% │ >Record Cr 0 0 ? ? │
│ BF3 ? -1 -1 1449669 79 99.99% │ DB Buf S Lock 1851338 0 100.00% │ Record Mo 0 0 ? ? │
│ BF1 ? -1 -1 1285001 71 99.99% │ Record Get 5 0 100.00% │ Record De 0 0 ? ? │
│ BHT ? -1 -1 1020388 40 100.00% │ Statement cach 0 0 ? │ Key Add 0 0 ? ? │
│ BF4 ? -1 -1 640121 33 99.99% │ Encryption buf 0 0 ? │ Key Delet 0 0 ? ? │
│ BF2 ? -1 -1 610660 28 100.00% │ DB Svc enqueue 0 0 ? │ Sequence 0 0 ? ? │
│ LKF ? 42 -1 11 0 100.00% │ Repl TEND Ack 0 0 ? │ Other 0 0 ? ? │
│ LHT ? 42 -1 4 0 100.00% │ TXE Excl Lock 0 0 ? │ Update Lo 0 0 ? ? │
│ LHT3 ? 42 -1 3 0 100.00% │ TXE Commit Loc 0 0 ? │ Commit Lo 0 0 ? ? │
│ LHT2 ? 42 -1 3 0 100.00% │ TXE Update Loc 0 0 ? │ │
│ LHT4 ? 42 -1 1 0 100.00% │ TXE Share Lock 0 0 ? │ │
│ RPL ? 0 -1 0 0 ? │ AI Buf Write 0 0 ? │ │
│ SEC ? -1 -1 0 0 ? │ AI Buf Read 0 0 ? │ │
│ CDC ? -1 -1 0 0 ? │ BI Buf Write 0 0 ? │ │
│ INC ? -1 -1 0 0 ? │ BI Buf Read 0 0 ? │ │
│ LRU2 ? -1 -1 0 0 ? │ DB Buf Write L 0 0 ? │ │
│ CPQ ? -1 -1 0 0 ? │ DB Buf X Lock 0 0 ? │ │
│ PWQ ? -1 -1 0 0 ? │ DB Buf S Lock 0 0 ? │ │
│ BFP ? -1 -1 0 0 ? │ DB Buf Avail 0 0 ? │ │
│ EC ? -1 -1 0 0 ? │ DB Buf X Lock 0 0 ? │ │
│ TXQ ? 42 -1 0 0 ? │ DB Buf Backup 0 0 ? │ │
│ AIB ? 0 -1 0 0 ? │ DB Buf Write 0 0 ? │ │

## Slide 13: Single Threaded Execution
Only one process can hold a latch at a time
So access to a latch forms a single-threaded bottleneck
You cannot process more latch requests for any one latch than one CPU core can handle

## Slide 14: Single Threaded Execution
Only one process can hold a latch at a time
So access to a latch forms a single-threaded bottleneck
You cannot process more latch requests for any one latch than one CPU core can handle
The only solutions are:
  Request fewer latches
  Spread locking over more latches
  Get faster cores

## Slide 15: Request Fewer Latches
-lruskips (later)
Fix your code ;)

## Slide 16: More Latches
Upgrade!
  Progress frequently improves the underlying algorithims to better spread things around
-hashLatchFactor
  Adjusts the number of BHT latches relative to -hash
Use more blocks
  BF* latches are actually one per block, smaller RPB spreads data over more blocks and thus more latches, but wastes a lot of space and memory. This really only works for very small yet very active tables.

## Slide 17: Faster Cores
Since the bottleneck is what a single core can execute you need faster cores to get more work done in less time
ADDITIONAL CORES WILL NOT HELP
Lots of slow cores does not help

## Slide 18: The Impact of Too Many Cores
Latches are frequently accessed memory locations
Which means that they are in the CPU cache…
… of every active core
Coordinating those caches across the bus is complex and expensive:
  Testing a value (reading it) is relatively cheap
  Updating it (setting it to a new value) is extremely expensive
  It is exponentially more expensive when the caches are on different chips or different CPU boards
  An update (someone succeeds in getting the latch) likely means that the pipelines on all of the other cores competing for the latch have mispredicted

## Slide 19: Too Many Cores II
You want to have your cores physically close to each other
Ideally in the same chip
Less ideally on the same board
The more distance signals have to travel and the more handoffs across the bus the worse performance will be
Modern operating systems try to ensure that the smallest number of cores are used and that they are “close” together – but virtualization often defeats this

## Slide 20: Some Important OpenEdge Latches
LRU - Least Recently Used block chain
MTX - Micro-transaction
BHT - Buffer Hash Table
OM - Object Manager
BF# - Buffer control
SEQ - Sequence Updates
LHT - Lock Hash Table (-L)
LKF - Lock Table Free List
LKP - Lock Purge Table

## Slide 21: What to do when you have naps on LRU?
-lruskips 10
Only update the LRU chain every 10th time a block is accessed
The order of the chain is no longer perfect
But that is more than good enough for most purposes
You quickly get to diminishing returns with large values
  Values > 100 are probably not going to be very meaningful
  Very small –B and very large –lruskips is probably not a good combination

## Slide 22: Updating the LRU Chain
Most Recently Used
Least Recently Used
Add a counter and only update every Nth block access

## Slide 23: What to do when you have naps on MTX?
MTX naps occur when committing data to disk
They are most frequently seen on slow, external disk subsystems
  SAN with RAID 5 for instance
Or review your code and reduce the rate at which you commit transactions
  Perhaps you have transaction scoping problems causing more commits than you expect

## Slide 24: What to do when you have naps on BHT?
You probably have some very high record read rates, millions per second
This is often due to poor WHERE clauses or poor index support for queries
If you cannot fix the code or add an index – faster cores are your best bet
OE11.7+ -hashLatchFactor may help

## Slide 25: What to do when you have naps on OM?
Object Manager cache
-omsize should be at least equal to the total number of tables, indexes and LOBs in your schema – including the metaschema

## Slide 26: BF1 <> BF2 <> BF3 <> BF4
The BF* latches are an accounting fiction
There is actually one such latch for every block in –B
But that would get messy to track so there are 4 “buckets”
  Normally the values for all 4 buckets are “close”
  If one of them consistently spikes then you may have a “hot spot”
  The chances are fairly good that the driver of that hot spot is an unusually active user/table/index

## Slide 27: Lots of Napping
Relatively high %sys
Increase -spin!

## Slide 28: CPU Exhaustion
You use up all of your CPU power
The number of latch requests plummets
But nobody is napping
-spin cannot complete before your process is rescheduled
Reduce -spin

## Slide 29
Questions?
Notes: And now we have some time for questions…

## Slide 30
Thank You!