## Slide 1: Barcodes
Bob Brennan
Integrated Manufacturing Systems, Inc.

## Slide 2: What is a bar code
A bar code is a method of representing data in a visual, machine-readable form.
Historically a set of parallel lines (1 – D)
Bar Code reader would interpret the bars

## Slide 3: Why Use a Bar Code
Timely
Accurate
Repeatable
Durable

## Slide 4: Type of Readers Connections
USB
Serial
Bluetooth
Embedded

## Slide 5: Scan Engines - Reading
Laser
CCD
Imagers

## Slide 6: Form Factors

## Slide 7: Types of Scan Engines
Near/Standard Range
  6” to Arms Length
Far Range
  Arms Length to 20 Feet
Ultra Far Range
  Arms Length to 75 under Specific Conditions
High Density
  Tiny bar codes like Printed Circuit Boards
Outdoors

## Slide 8: How a Reader Works
Physics 101
Light Shines
Reflection
Inverse is Read
Pattern Recognized
Converted Output

## Slide 9: Types of Bar Codes

## Slide 10: Symbologies
Set of Rule
Character Sets
Control Codes
Start/Stop bits
Check Digit
Contract between the creator and consumer

## Slide 11: Encoding Methods
Linear – One Character = Set of Bars
Interleaved = String of Characters compressed
Look Up Tables – Characters have fixed Representations that follow a defined scheme
Limited Character Sets

## Slide 12: X-Dimension

## Slide 13: X-Dimension 2D

## Slide 14: X-Dimension Math
Symbology determines the Characters allowed
X-Dimension establishes the width
All Bar widths are a multiple X-Dim
Linear Growth

## Slide 15: 1 D Bar Code
Typically represents a single data element
Not a lot of symbologies allow control codes
You can make up a concatenation scheme
Match your need to the best Symbology

## Slide 16: 2 D Bar Codes
More of a paragraph or document model
Creator and Generator agree to what separates fields and records.
Both implement the same for the other’s benefit
Business document trading facility
QR Codes are a free form symbology.

## Slide 17: What could go Wrong Reading
Lack of Light
Diffraction/Deflection
X-Dimension
Quit Zone Violation
Wrong Scan Engine

## Slide 18: Error Correction (The AI Slide)
Smeared
Wrinkled
Torn
Print Head Damage
Shrink Wrapped over Label
Stretched
Obscured

## Slide 19: Adjacent Technologies
Direct Part Marking
Peening Dot Scribing

## Slide 20: Reader Connectivity Options
USB as HID Includes Blue Tooth
  Keyboard Wedge
  Typing is the same as scanning is the same as typing
  All the traffic and Buffering is done for you
Serial
  All the old issues Baud Rate, Parity XON/Xoff, Buffering
Embedded
  Usually HID or as a web service

## Slide 21: How to Generate a Bar Code
Fonts
Code to a Printer Specific Language
Use a tool
  Loftware
  Generator Websites – Ask The Google
  Bartender
  Nice Label

## Slide 22: How to Print
Embedded in a normal document
  Word or Excel or Crystal Reports …
QR Code Generators et.al.
Label Printer
  Direct Thermal
  Thermal Transfer
Specialty - Card and Badge Printers

## Slide 23: Label Stock and Reader
Paper
Laminates
Permanent
Retro-Reflective

## Slide 24: Sense of the Room
Acknowledgement of our Quaker Friends.

## Slide 25: Scanning Demo

## Slide 26: RFID

## Slide 27: Active Tags – Self Powered

## Slide 28: Passive Tags – No Power

## Slide 29: Physical Tag

## Slide 30: Industrial Engineering
Reader Location
Point in time versus direction
Placement of Tag
Physics of Tag Radio Propagation

## Slide 31: Bob Brennan Integrated Manufacturing Systems, Inc. (603) 424-0109